HWLoc Tcl Binding GSoC 2011 Project
API Design, Version 0.5

# API Version
Pertains the following HWLoc Module(s):
API version
## hwloc version
Description: Indicate at runtime which hwloc API version was used at build time.
Returns: Unsigned integer.
Underlying function(s):
unsigned hwloc_get_api_version (void)
# Create, Configure, Check and Destroy Topologies
Pertains the following HWLoc Module(s):
- Topology context
- Create and Destroy Topologies
- Configure Topology Detection
Non-implemented functions:
- int hwloc_topology_set_xmlbuffer (hwloc_topology_t __hwloc_restrict topology, const char *__hwloc_restrict buffer, int size)
- int hwloc_topology_set_distance_matrix (hwloc_topology_t __hwloc_restrict topology, hwloc_obj_type_t type, unsigned nbobjs, unsigned *os_index, float *distances)
- struct
  hwloc_topology_support * hwloc_topology_get_support (hwloc_topology_t __hwloc_restrict topology)
## hwloc create ?options?
Description: Initialize, load and check a new topology context according to ?options?:
-ignore_type $type
-ignore_type_keep_structure
-ignore_all_keep_structure
-set_flags $flags
-set_fsroot $path
-set_pid $pid
-set_synthetic $string
-set_xml $filepath
Returns: A new command that embodies the topology context.
Underlying function(s):
- int hwloc_topology_init (hwloc_topology_t *topology)
- int hwloc_topology_load (hwloc_topology_t topology)
- void hwloc_topology_check (hwloc_topology_t topology)
- int hwloc_topology_ignore_type (hwloc_topology_t topology, hwloc_obj_type_t type)
- int hwloc_topology_ignore_type_keep_structure (hwloc_topology_t topology, hwloc_obj_type_t type)
- int hwloc_topology_ignore_all_keep_structure (hwloc_topology_t topology)
- int hwloc_topology_set_flags (hwloc_topology_t topology, unsigned long flags)
- int hwloc_topology_set_fsroot (hwloc_topology_t __hwloc_restrict topology, const char *__hwloc_restrict fsroot_path)
- int hwloc_topology_set_pid (hwloc_topology_t __hwloc_restrict topology, hwloc_pid_t pid)
- int hwloc_topology_set_synthetic (hwloc_topology_t __hwloc_restrict topology, const char *__hwloc_restrict description)
- int hwloc_topology_set_xml (hwloc_topology_t __hwloc_restrict topology, const char *__hwloc_restrict xmlpath)
## topology destroy
Description: Terminate and free a topology context. Also destroy the corresponding Tcl command.
Returns: Nothing.
Underlying function(s):
void hwloc_topology_destroy (hwloc_topology_t topology)
# Get Topology Information
Pertains the following HWLoc Module(s):
- Tinker with topologies.
- Get some Topology Information
- Retrieve Objects
Non-implemented functions:
- void hwloc_topology_export_xmlbuffer (hwloc_topology_t topology, char **xmlbuffer, int *buflen)
- void hwloc_topology_export_xmlbuffer (hwloc_topology_t topology, char **xmlbuffer, int *buflen)
- hwloc_obj_t hwloc_topology_insert_misc_object_by_parent (hwloc_topology_t topology, hwloc_obj_t parent, const char *name)
- int hwloc_topology_restrict (hwloc_topology_t __hwloc_restrict topology, hwloc_const_cpuset_t cpuset, unsigned long flags)
## topology export filepath
Description: Export the topology into an XML file.
Returns: Nothing.
Underlying function(s):
void hwloc_topology_export_xml (hwloc_topology_t topology, const char *xmlpath)

## topology depth
Description: Get the depth of the hierarchical tree of objects.
Returns: Unsigned integer.
Underlying function(s):
unsigned hwloc_topology_get_depth (hwloc_topology_t __hwloc_restrict topology) __hwloc_attribute_pure

## topology depth -type type
Description: Returns the depth of objects of type type.
Returns: Unsigned integer.
Underlying function(s):
int hwloc_get_type_depth (hwloc_topology_t topology, hwloc_obj_type_t type)

## topology type -depth depth
Description: Returns the type of objects at depth depth.
Returns: String representation of topology object type.
Underlying function(s):
hwloc_obj_type_t hwloc_get_depth_type (hwloc_topology_t topology, unsigned depth)

## topology width -depth depth
Description: Returns the width of level at depth depth.
Returns: Unsigned integer.
Underlying function(s):
unsigned hwloc_get_nbobjs_by_depth (hwloc_topology_t topology, unsigned depth)

## topology width -type type
Description: Returns the width of level type type.
Returns: Unsigned integer.
Underlying function(s):
static __hwloc_inline int
__hwloc_attribute_pure hwloc_get_nbobjs_by_type (hwloc_topology_t topology, hwloc_obj_type_t type)
## topology local
Description: Does the topology context come from this system?
Returns: Boolean.
Underlying function(s):
int hwloc_topology_is_thissystem (hwloc_topology_t __hwloc_restrict topology)
# Browse the Topology Tree
Pertains the following HWLoc Module(s):
Retrieve Objects
## topology root
Description: Returns the object at the root of the topology tree.
Returns: An object id.
Underlying function(s):
hwloc_obj_t hwloc_get_obj_by_depth (hwloc_topology_t topology, unsigned depth, unsigned idx)
## topology object_by {-depth depth | -type type} index
Description: Returns the object at depth depth or type type with index index.
Returns: An object id.
Underlying function(s):
- hwloc_obj_t hwloc_get_obj_by_depth (hwloc_topology_t topology, unsigned depth, unsigned idx)
- hwloc_get_obj_by_type (hwloc_topology_t topology, hwloc_obj_type_t type, unsigned idx)
## topology object object children
Description: Returns a list with all child objects of object object.
Returns: A list of object ids.
Underlying function(s):
hwloc_obj_t.children
## topology object object parent
Description: Returns the parent object or empty string if object is the root.
Returns: An object id.
Underlying function(s):
hwloc_obj_t.parent
## topology object object next_cousin | prev_cousin
Description: Returns next/previous object of same type and depth.
Returns: An object id.
Underlying function(s):
- hwloc_obj_t.next_cousin
- hwloc_obj_t.prev_cousin
## topology object object next_sibling | prev_sibling
Description: Returns next/previous object below the same parent.
Returns: An object id.
Underlying function(s):
- hwloc_obj_t.next_sibling
- hwloc_obj_t.prev_sibling
## topology object object first_child | last_childy
Description: Returns first/last child.
Returns: An object id.
Underlying function(s):
- hwloc_obj_t.first_child
- hwloc_obj_t.last_child
# Get Object Information
## topology object object type
Description: Returns object's type.
Returns: A special string constant that represents the type of the object.
Underlying function(s):
hwloc_obj_t.type
## topology object object name
Description: Returns object's name.
Returns: String.
Underlying function(s):
hwloc_obj_t.name
## topology object object depth
Description: Returns object's depth.
Returns: Number.
Underlying function(s):
hwloc_obj_t.depth
## topology object object logical_index
Description: Horizontal index in the whole list of similar objects, could be a "cousin_rank" since it's the rank within the "cousin" list below.
Returns: Number.
Underlying function(s):
hwloc_obj_t.logical_index
## topology object object sibling_rank
Description: Index in parent's children[] array.
Returns: Number.
Underlying function(s):
hwloc_obj_t.sibling_rank
## topology object object arity
Description: Returns number of object's children.
Returns: Number.
Underlying function(s):
hwloc_obj_t.arity
## topology object object attributes
Description: Object type-specific attributes.
Returns: String.
Underlying function(s):
hwloc_obj_t.attr
## topology object object cpuset
Description: CPUs covered by this object.
Returns: Hex string.
Underlying function(s):
hwloc_obj_t.cpuset
## topology object object info
Description: List of infos for the object in {name value} format.
Returns: List of lists.
Underlying function(s):
hwloc_obj_t.infos
# CPU Binding
Pertains the following HWLoc Module(s):
CPU binding

Notes:
- “flags” is a list of: “process”, “thread”, “strict”, “nomembind” string elements.
- “cpuset” is a string of comma-separated indexes or ranges. Ranges are dash separated indexes. The last range may not have a ending indexes if the cpuset is infinite. For instance: “0-1,3,7-”.
## topology cpubind set ?-type flags? ?-pid pid? cpuset
Description: Bind current or specified process or thread on cpus given in cpuset.
Returns: Nothing.
Underlying function(s):
- int hwloc_set_cpubind (hwloc_topology_t topology, hwloc_const_cpuset_t set, int flags)
- int hwloc_set_proc_cpubind (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_const_cpuset_t set, int flags)
- int hwloc_bitmap_list_asprintf (char **strp, hwloc_const_bitmap_t bitmap)
## topology cpubind get ?-type flags? ?-pid pid?
Description: Get current process or thread binding, or that of the specified process.
Returns: String representation of a cpuset .
Underlying function(s):
- int hwloc_get_cpubind (hwloc_topology_t topology, hwloc_cpuset_t set, int flags)
- int hwloc_get_proc_cpubind (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_cpuset_t set, int flags)
- int hwloc_bitmap_list_sscanf (hwloc_bitmap_t bitmap, const char *__hwloc_restrict string)
## topology cpubind last ?-type flags? ?-pid pid?
Description: Get the last CPU where the current process or thread ran, or that of the specified process.
Returns: String representation of a cpuset .
Underlying function(s):
- int hwloc_get_last_cpu_location (hwloc_topology_t topology, hwloc_cpuset_t set, int flags)
- int hwloc_get_proc_last_cpu_location (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_cpuset_t set, int flags)
- int hwloc_bitmap_list_sscanf (hwloc_bitmap_t bitmap, const char *__hwloc_restrict string)
# The Bitmap API
Pertains the following HWLoc Module(s):
The bitmap API
XXX
# Memory Binding
Pertains the following HWLoc Module(s):
Memory binding
## topology membind get ?-pid pid? ?-type flags? ?-cpuset?
Description: Query the default memory binding policy and locality of the current process (or the specified one with -pid) or thread. If -cpuset is specified, then the returned bitmap are the CPUs near the locality's actual NUMA node(s).
Returns: String representation of a noteset.
Underlying function(s):
- int hwloc_get_membind_nodeset (hwloc_topology_t topology, hwloc_nodeset_t nodeset, hwloc_membind_policy_t *policy, int flags)
- int hwloc_get_membind (hwloc_topology_t topology, hwloc_cpuset_t cpuset, hwloc_membind_policy_t *policy, int flags).
- int hwloc_get_proc_membind_nodeset (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_nodeset_t nodeset, hwloc_membind_policy_t *policy, int flags)
- int hwloc_get_proc_membind (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_cpuset_t cpuset, hwloc_membind_policy_t *policy, int flags)
## topology membind set ?-pid pid? ?-type flags? ?-cpuset? nodeset policy
Description: Set the default memory binding policy of the current (or the specified one with -pid) process or thread to prefer the NUMA node(s) specified by nodeset. If -cpuset is specified, then the binding is near the specified CPUs in bitmap.
Returns: Nothing.
Underlying function(s):
- int hwloc_set_membind_nodeset (hwloc_topology_t topology, hwloc_const_nodeset_t nodeset, hwloc_membind_policy_t policy, int flags)
- int hwloc_set_membind (hwloc_topology_t topology, hwloc_const_cpuset_t cpuset, hwloc_membind_policy_t policy, int flags)
- int hwloc_set_proc_membind_nodeset (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_const_nodeset_t nodeset, hwloc_membind_policy_t policy, int flags)
- int hwloc_set_proc_membind (hwloc_topology_t topology, hwloc_pid_t pid, hwloc_const_cpuset_t cpuset, hwloc_membind_policy_t policy, int flags)
# Helpers
Pertains the following HWLoc Module(s):
- Cpuset Helpers
- Nodeset Helpers
- Conversion between cpuset and nodeset
## topology cpuset ?-complete|-allowed|-online|-topology?
Description: Get complete/allowed/online/topology CPU set.
Returns: A cpuset string representation.
Underlying function(s):
- hwloc_const_cpuset_t
  __hwloc_attribute_pure hwloc_topology_get_complete_cpuset (hwloc_topology_t topology)
- hwloc_const_cpuset_t
  __hwloc_attribute_pure hwloc_topology_get_topology_cpuset (hwloc_topology_t topology)
- hwloc_const_cpuset_t
  __hwloc_attribute_pure hwloc_topology_get_online_cpuset (hwloc_topology_t topology)
- hwloc_const_cpuset_t
  __hwloc_attribute_pure hwloc_topology_get_allowed_cpuset (hwloc_topology_t topology)
## topology nodeset ?-complete|-allowed|-topology?
Description: Get complete/allowed/topology NODE set.
Returns: A nodeset string representation.
Underlying function(s):
- hwloc_const_nodeset_t
  __hwloc_attribute_pure hwloc_topology_get_complete_nodeset (hwloc_topology_t topology)
- hwloc_const_nodeset_t
  __hwloc_attribute_pure hwloc_topology_get_topology_nodeset (hwloc_topology_t topology)
- hwloc_const_nodeset_t
  __hwloc_attribute_pure hwloc_topology_get_allowed_nodeset (hwloc_topology_t topology)
## topology convert ?-strict? -to_cpuset|-to_nodeset bitmap
Description: Convert cpuset to NUMA nodeset and vise versa, which optionally handling non-NUMA cases.
Returns: A cpuset string representation.
Underlying function(s):
- hwloc_cpuset_to_nodeset (hwloc_topology_t topology, hwloc_const_cpuset_t cpuset, hwloc_nodeset_t nodeset)
- hwloc_cpuset_to_nodeset_strict (struct hwloc_topology *topology, hwloc_const_cpuset_t cpuset, hwloc_nodeset_t nodeset)
- hwloc_cpuset_from_nodeset (hwloc_topology_t topology, hwloc_cpuset_t cpuset, hwloc_const_nodeset_t nodeset)
- hwloc_cpuset_from_nodeset_strict (struct hwloc_topology *topology, hwloc_cpuset_t cpuset, hwloc_const_nodeset_t nodeset)
# Remaining Modules
- Various Helpers
  - Object Type Helpers
  - Basic Traversal Helpers
  - Advanced Traversal Helpers
  - Binding Helpers
- Finding Objects
  - Finding Objects Inside a CPU set
  - Finding a single Object covering at least CPU set
  - Finding a set of similar Objects covering at least a CPU set
  - Cache-specific Finding Helpers
- Distances